| MIFAB, Inc. | July 2008 |
| --- | --- |
| 1321 West 119th Street |  |
| Chicago, IL 60643-5109 |  |
| Toll Free (800) 465-2736 |  |
| Phone (773) 341-3030 | E-Mail mail@mifab.com |
| Fax (773) 341-3049 | Web Site www.mifab.com |

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the drawings. Delete all “Specifier Notes” when editing this section.

SECTION 22150

FLOOR CLEANOUTS

Specifier Notes: This section covers MIFAB “C1100-R” adjustable floor cleanout for non-membrane floor areas. Consult MIFAB for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Adjustable floor cleanout for non-membrane floor areas.

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 22100 - Building Services Piping.

B.	Section 22400 - Plumbing Fixtures and Equipment.

1.3	REFERENCES

A.	ANSI/ASME A112.36.2M - Cleanouts.

B.	ASTM A 48 - Standard Specification for Gray Iron Castings.

1.4	SUBMITTALS

A.	Comply with Section 01330 - Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including installation instructions.

1.5	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.

C.	Handling:  Protect materials and finish from damage during handling and installation.

PART 2	PRODUCTS

2.1	MANUFACTURER

Specifier Notes: Specify MIFAB, Inc. in the US or MIFAB Canada in Canada

A.	[MIFAB, Inc., 1321 West 119th Street, Chicago, IL. 60643-5109  Toll Free (800) 465-2736.]

Web Site www.mifab.com  E-Mail mail@mifab.com.

2.2	MATERIALS

A.	Floor Cleanouts:  Adjustable floor cleanout for non-membrane floor areas.

1.	Compliance:  ANSI/ASME A112.36.2M.

Specifier Notes: Specify required floor cleanouts by type of floor or flooring material. Add “C” after “C1100” to each of the series numbers below when cleanouts in waterproofed floors are required.

2.	Cleanouts in Finished Floors:  [C1100-R, round top,]  [C1100-S, square top,] nickel bronze, satin finish.  Load rating of up to 4,999 pounds.

3.	Cleanouts in Finished Floors:  C1100-XR, round, heavy-duty, 1/2-inch (13-mm) thick top, nickel bronze, satin finish.  Load rating of up to 7,499 pounds.

4.	Cleanouts in Unfinished Areas:  C1100-XR-4, round top, ductile iron cover.  Load rating of up to 7,499 pounds.

5.	Cleanouts in Resilient Tile Flooring Areas:  [C1100-T-1, round top,]  [C1100-TS-1, square top,] nickel bronze, satin finish.  Load rating of up to 4,999 pounds.

6.	Cleanouts in Ceramic or Terrazzo Areas:  [C1100-UR-1, round top,]  [C1100-US-1, square top,] nickel bronze, satin finish.  Load rating of up to 4,999 pounds.

7.	Cleanouts in Carpeted Areas:  C1100-RC-1, round top, nickel bronze, satin finish.  Stainless steel carpet marker.  Load rating of up to 4,999 pounds.

8.	Cleanouts in Waterproofed Floors:  As specified, except with integral membrane clamp ring for waterproofing membrane.

9.	Body:  A1, 8-inch (200-mm) diameter body.  Lacquered, ASTM A 48, Class 25 cast iron body with anchor flange.  O-ring secondary gasket seal.  4-inch (100-mm) throat.  4-inch (100-mm) NPS machined integral body threads.

10.	Combined Access Cover and Plug Top Assembly:  Round, 5-inch (125-mm) diameter, adjustable.  Neoprene primary gasket seal.  Vandal-resistant stainless steel screws.

Specifier Notes: Specify pipe size.

11.	Pipe Size:  [2 inches (50 mm)]  [3 inches (75 mm)]  [4 inches (100 mm)]  [6 inches (150 mm)].

Specifier Notes: Specify required floor cleanout options and revise above text as necessary. Delete options not required. Consult MIFAB for additional information.

B.	Floor Cleanout Options:

1.	Top Assembly:  [Type 304 stainless steel]  [Ductile iron for unfinished areas].

2.	3M epoxy finish.

3.	Vandal proof.

4.	Acid-resistant epoxy coating.

5.	All galvanized.

6.	Body:  [Bronze]  [Type 304 stainless steel]  [Type 316 stainless steel].

7.	Socket Connection Body:  [PVC]  [ABS].

8.	Secondary plug.

9.	Client logo.

10.	Floating slab variation.

11.	Outlet:  [Push-on]  [Threaded]  [Inside caulk].

12.	Stainless steel carpet marker.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive floor cleanouts.  Notify Architect of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install floor cleanouts in accordance with manufacturer's instructions at locations indicated on the drawings.

B.	Install floor cleanouts plumb, level, and to correct elevation.

C.	Ensure top of floor cleanouts are flush with top of finished floor.

Specifier Notes: Specify the following sentence when specifying square top assembly floor cleanouts.

D.	Align sides of square cleanouts parallel with adjacent walls and pattern of flooring materials.

E.	Install floor cleanouts using manufacturer's supplied hardware.

3.3	PROTECTION

A.	Protect installed floor cleanouts from damage during construction.

END OF SECTION