# Plumbing Drainage & Specialties - Specification

For Commercial, Industrial & Institutional Facilities

Specification  Category		Description

“TSP”

Trap Seal Primers	(Continuous Flow)

Trap Seal Primers	(Pressure Drop Activated)

Trap Seal Primers	(Distribution Manifold)

Trap Seal Primers	(Connection Adapters)

### TRAP SEAL PRIMERS

TP1	TRAP SEAL PRIMERS – CONTINUOS FLOW

MIFAB model MI-TSP-1 brass trap seal primer with removable poppet, integral vacuum breaker, gasketed access cover, 1/2" (13) N.P.T. inlet and outlet connections, complete with 1/2" (13) sweat connection adaptors and 1/2" (13) drip line connection.

TP2	TRAP SEAL PRIMERS – PRESSURE DROP TYPE

M-500 Series - Pressure Drop Activated Trap Seal Primer

MIFAB model MR-500 pressure drop activated brass trap seal primer, with inlet opening of 1/2" (13) male N.P.T. and outlet opening of female 1/2" (13) N.P.T.  Complete with four view holes and removable filter

screen. Serves up to 6 floor drain traps and requires no adjustments and no air pre-charge.

MIFAB model M1-500 pressure drop activated brass trap seal primer, with inlet opening of 1/2" (13) male N.P.T. and outlet opening of female 1/2" (13) N.P.T.  Complete with four view holes and removable filter screen. Serves up to 10 floor drain traps and requires no adjustments and no air pre-charge.

MIFAB model M2-500 pressure drop activated brass trap seal primer, with inlet opening of 1/2" (13) male N.P.T. and outlet opening of female 1/2" (13) N.P.T.  Complete with four view holes and removable filter screen. Serves up to 3 floor drain traps and requires no adjustments and no air pre-charge.

TP3	TRAP SEAL PRIMERS – DISTRIBUTION MANIFOLD

MIFAB model MI-DU trap seal primer distribution unit with four 3/8" (10) F.P.T. brass nipple outlet connections to serve either 2, 3, or 4 floor drain traps and a 1/2" (13) M.P.T. inlet connection.  Unit complete with four 1/4" (6) diameter vent holes in the lid and three 1/8" (3) diameter Phillips Head screws to secure the lid to the body.

TP4   	 TRAP SEAL PRIMER – CONNECTION ADAPTERS

MIFAB Series MI-6 __ ABS or PVC (specify) schedule #40 D.W.V. P-Trap trap seal primer connector, with 2" (50) 3" (75), or 4" (100) (specify) pipe connections, and a 1/2" (13) or 5/8" (16) (specify) brass compression fitting connection to attach to a trap seal primer water supply line.  The MIFAB MI-600 Series of P-Trap trap seal primer connectors meet the ASTM D-2661 and ASTM D-2665 Standards.