# Plumbing Drainage & Specialties - Specification

For Commercial, Industrial & Institutional Facilities

Specification  Category		Description

“INT”

Interceptors		(Grease Interceptor - Standard)

Interceptors		(Grease Interceptor - Low Rough-In)

Interceptors		(Grease Interceptor - Electronic)

Interceptors		(Oil Interceptor - Standard)

Interceptors		(Oil Interceptor - c/w Integral Holding Tank)

Interceptors		(Oil Interceptor - Electronic)

Interceptors		(Sediment - Large)

Interceptors		(Sediment - Medium)

Interceptors		(Sediment – Small)

Interceptors		(Hair)

### INTERCEPTORS

INT1	INTERCEPTORS – GREASE INTERCEPTOR – STANDARD

MIFAB Series MI-G sanitary powder epoxy coated inside and outside fabricated 10 gauge steel grease interceptor with flow rating of ___ (indicate) and grease holding capacity of ____ (indicate).

Unit shall include:  removable baffle assembly and cross bar, deep seal trap covered by lid, securing bolt(s), flow control fitting, internal air relief bypass and steel powder epoxy coated, non skid, rectangular gasketed lid(s).  Interceptor shall be tested and certified to the P.D.I. standard PDI-G101 and be so marked.

INT2	INTERCEPTORS – GREASE INTERCEPTOR – LOW ROUGH IN

MIFAB Series MI-G-L __ sanitary powder epoxy coated inside and outside fabricated 10 gauge steel grease interceptor with flow rating of ___ indicate) and grease holding capacity of ____ (indicate).

Unit shall include:  removable baffle assembly and cross bar, securing bolt(s), flow control fitting, internal air relief bypass and steel powder epoxy coated rectangular gasketed lid.

INT3	INTERCEPTORS – GREASE INTERCEPTOR – ELECTRONIC

Mifab Series ME-G ____ (Specify Size) Electronic Grease interceptors to be of fabricated 10 gage epoxy coated steel construction with failsafe electronic controls, including 115/24 VAC 12 VA, class II transformer, epoxy encapsulated multi-level probe assembly, failsafe knife edge valve on inlet side, compact control panel with 3 position switch, multilevel LED display, diagnostic LED’s audible alarm and auxillary contacts for remote alarm/control functions.  Unit shall include:  removable baffle assembly and cross bar, deep seal trap covered by lid, securing bolt(s), flow control fitting, internal air relief bypass and

epoxy coated steel non skid, rectangular gasketed lid(s).  Interceptor extensions to be supplied as required.

INT4	INTERCEPTORS – OIL INTERCEPTOR – STANDARD

MIFAB Series MI-O __ (Specify Size)sanitary powder epoxy coated inside and outside fabricated 10 gauge steel oil interceptor.

Unit to include:  sediment bucket with perforated baffle near inlet, deep seal trap covered by lid, securing bolt(s), removable baffle assembly and cross bar, stainless steel calibrated orifice plate, adjustable automatic draw-off assembly, double vent connections on each side, and steel powder epoxy coated non skid rectangular lid.

INT5	INTERCEPTORS – OIL INTERCEPTOR – C/W INTEGRAL HOLDING TANK

MIFAB Series MI-O-HU __ (Specify Size) sanitary powder epoxy coated inside and outside fabricated 10 gauge steel oil interceptor.

Unit to include:  sediment bucket with perforated baffle near inlet, deep seal trap covered by lid, securing bolt(s), removable baffle assembly and cross bar, stainless steel calibrated orifice plate, adjustable automatic draw-off assembly, double vent connections on each side, and steel powder epoxy coated non skid rectangular lid(s). Unit comes complete with integral holding tank for additional waste oil storage.

INT6	INTERCEPTORS – OIL INTERCEPTOR – ELECTRONIC

MIFAB ME-O ____ (Specify Size) Electronic Oil interceptor to be of fabricated 10 gage epoxy coated steel construction with failsafe electronic controls, including 115/24 VAC 12 VA, class II transformer, epoxy encapsulated multi-level probe assembly, failsafe knife edge valve on inlet side, compact control panel with 3 position switch, multilevel LED display, diagnostic LED’s audible alarm and auxillary contacts for remote alarm/control functions.  Unit to include:  sediment bucket with perforated baffle near inlet, deep seal trap covered by lid, securing bolt(s), removable baffle assembly and cross bar, stainless steel calibrated orifice plate, adjustable automatic draw-off assembly, double vent connections on each side, and epoxy coated steel non skid rectangular lid(s).

INT7	INTERCEPTORS – SEDIMENT – LARGE

MIFAB Series MI-SOLID-L sanitary powder epoxy coated inside and outside fabricated 10 gauge steel solids interceptor.

Unit shall include:  removable perforated sediment screen with bucket and a steel powder epoxy coated, non skid, rectangular gasketed cover, secured by a single recessed bolt.

INT8	INTERCEPTORS – SEDIMENT – MEDIUM

MIFAB Series MI-SOLID-M sanitary powder epoxy coated inside and outside fabricated 10 gauge steel solids interceptor.

Unit shall include:  removable perforated sediment screen with bucket and a steel powder epoxy coated, non skid, rectangular gasketed cover, secured by a single recessed bolt.

INT9	INTERCEPTORS – SEDIMENT – SMALL

MIFAB Series MI-SOLID-S sanitary powder epoxy coated inside and outside fabricated 10 gauge steel solids interceptor.

Unit shall include:  removable perforated sediment screen with bucket and a gasketed steel lid secured by a single recessed bolt.

INT10	INETERCEPTORS – HAIR

MIFAB Series MI-HAIR sanitary epoxy coated inside and outside cast iron hair interceptor.

Unit shall include:  1-1/2" (38) slip joint elbow inlet and 1-1/2" (38) threaded side outlet, perforated basket removable from bottom, with gasketed cleanout cover.