SECTION 07 70 00

ROOF ACCESSORIES

Applicable to Section 23000 (mechanical) 22000 (plumbing).

PART 1 GENERAL

1.01 	SECTION INCLUDES

A.	The work covered by this specification consists of furnishing all labor, equipment,

materials and accessories, and performing all operations required for the correct

installation of recycled rubber pipe supports for mechanical piping

systems.

1.02	REFERENCES

A.	ASTM A653 G90 SS Gr. 33 - Specification for Steel Sheet, Zinc Coated

(Galvanized) by the Hot Dipped Process

B.	ASTM B633 - Specification for Electrodeposited Coatings of Zinc on Iron and

Steel

C.	ASTM C531 – Test Method for Linear Shrinkage and Coefficient of Thermal Expansion of Chemical Resistant Mortars, Grouts, Monolithic Surfaces, and Polymer Concretes

D.	ASTM C642 – Test Method for Specific Gravity, Absorption, and Voids in Hardened Concrete

E.	ASTM C672 – Test Methods for Scaling Resistance of Concrete Surfaces Exposed to Deicing Chemicals

F.	ASTM D412 – Test Methods for Vulcanized Rubber and Thermoplastic Elastomers – Tension

G.	ASTM D395 – Standard Test Methods for Rubber Property – Compression Set

H.	ASTM D573 – Test Method for Rubber – Deterioration in an Air Oven

I.	ASTM D746 – Test Method for Brittleness Temperature of Plastics and Elastomers by Impact

J.	ASTM D2240 – Test Method for Rubber Property – Durometer Hardness

K.	NFPA 70 – National Electrical Code

1.03	QUALITY ASSURANCE

A.	Rubber / steel pipe supports shall be manufactured under a strict quality control program assuring quality product delivered to the jobsite. Pipe supports that are damaged shall not be installed.

B.	Workmanship: All pipe [conduit] supports to be installed by a qualified piping [electrical] contractor and installed in accordance with manufacturer’s recommendations.

1.  All work shall comply with all applicable federal, state, and local codes and

laws having jurisdiction.

- All work shall conform to accepted industry and trade standards for pipe

support [conduit] installations.

PART 2 PRODUCTS

2.01  	ACCEPTABLE MANUFACTURERS

A.	Manufacturer:  Subject to compliance with these specifications, pipe support systems shall be C-Port™ design as supplied by Clearline Technologies [or engineer approved equal].

2.02  	MATERIALS

A.	Curb base must be made of 100% recycled rubber and polyurethane prepolymer with a uniform load capacity of 500 pounds per linear foot of support*.  In addition, each base to have a reflective yellow stripe.(*See 3.01(C))

B.	Dimensions: 6-inches wide by [4] [5.0] [6.75] inches tall by [9.6] [19.2] [28.8] [38.5] [48.0] inches long.

C.	Steel frame: Steel, strut galvanized per ASTM A653 or strut galvanized per ASTM A653 for bridge series.

D.	Attaching hardware: Zinc-plated threaded rod, nuts and attaching hardware per ASTM B633.

E.	Any products claiming to be a similar, like, or equal must demonstrate (meet or exceed) the same physical and performance characteristics as specified below:

1.  Density:     0.52 oz/cu in     ASTM D575

2.  Durometer Hardness:     67.2A ± 1     ASTM D575

3.  Tensile Strength:     250 psi minimum     ASTM D575

4.  Compression Deformation:     5% at 70psi and 72ºF     ASTM D395

5.  Brittleness at Low Temp:     -50ºF     ASTM D746

6.  Weathering:     70 hours at 120ºF     ASTM D573

a.  Hardness retained:     100% (±5%)

b.  Compressive strength:     100% (±5%)

c.  Tensile strength:     100% (±5%)

d.  Elongation retained:     100% (±5%)

2.03  	TYPE OF ROOFTOP SUPPORTS

- Rubber block supports – C-Port™ model # [CXP] [CXM] base dimensions: 6-inch wide by 4-inch tall by [9.6] [5]-inch length.  Accessories are fastened directly into rubber material with weather resistant type 12 lag screws.

- Rubber block wide supports – C-Port™ model # CXW base dimensions; 12-inch wide by 2.5-inch tall by 12-inch length.  Accessories are fastened directly into rubber material with weather resistant type 12 lag screws.

- Continuous block channel supports – C-Port™  C-Series or C6-Series:

Dimensions 6-inch wide by [5.0] [6.5]-inch tall by [5] [9.6] [19.2] [28.8] [38.5] [48]-inch length. Standard strut accessories can be used for attachment.

- Continuous wide block channel supports – C-Port™  CW-Series

Dimensions 12-inch wide by 3.3-inch tall by [12] [24] [36] [48] [60] [72]-inch length. Standard strut accessories can be used for attachment.

- Bridge channel supports – C-Port™  CB-Series; Dimensions 6-inch wide by       5-5/8-inch tall by [28] [36] [42] [50] [60]-inch length. Standard strut

accessories can be used for attachment.

- Extendible height support – C-Port™ model CE10-[8][12][16], height to suit application: 8-inch, 12-inch or 16-inch (400 pound maximum load).  Base to be 9.6 inches in length or otherwise specified sizes available.

- Extendible height support – C-Port™ model CEW12-[8][12][16][24], height to suit application: 8-inch, 12-inch, 16-inch or 24-inch (800 pound maximum load).  Base to be 12 inches in length or otherwise specified sizes available.

- Roller supports for smaller pipes– C-Port™ CRM Series sized for [1] [2]

[3] [4] inch pipe sizes. With adjustability in height by 1”.  Roller supports– C-Port™ CR10 Series sized for [3] [4] pipe sizes.

- Extendable height Roller supports– C-Port™ CRE Series & CREW Series:         CRE Series is sized for pipe up to 4 inches, with vertical adjustment up to 12 inches.  CREW Series is sized for [3] [4] [6] [8-10] inch pipe sizes.

- Gasket Series Support – C-Port™ model CGW-Series; Dimensions 12-inch wide by 3.3-inch tall by [12] [24] [36] [48] inch length. With roofing membrane [EPDM] [TPO] [PVC] mechanically fastened to support.  Standard strut accessories can be used for attachment.

- Vari-Angle Support - C-Port™ model CS-Series; Dimensions 6-inch wide by 5.6-inch tall by [9.6] [19.2] [28.8] [38.5] [48]-inch length. With vari-angle adapter leg to accommodate 1-5/8-inch strut.

- Slip Sheets - C-Port™ Slip Sheets [EPDM] [TPO] [PVC] to be installed where further membrane protection is needed; Dimensions [12] [18]-inch wide by .060-inch thick by [16] [18]-inch length.

PART 3 EXECUTION

3.01 	INSTALLATION

- Install in accordance with manufacturer’s instructions and recommendations.

- If gravel top roof, gravel must be removed around and under pipe support.

- If necessary, a compatible sheet of roofing material (rubber pad) may be installed under rooftop support to disperse concentrated loads and add further membrane protection.

- Always consult roofing manufacturer for roof membrane compression capacities.

- Always install within the PSI roof rating.

- Gas pipe spacing subject to local gas authorities.

- Use properly sized clamps to suit pipe sizes.

END OF SECTION